## Slide 1: User Guide Filter Press Operation

## Slide 2
Contents
4-5. First Time Startup
  Description of Operation
  Setting Move Positions
Home Screen
  Layout
  Manual/Auto/Cycle Stop
5. Settings
  Conveyors
    Speed
  Gantry
    Position Settings
  Filter Plate
    Position Settings
  Press Settings
    Position Settings
    Speed
  Maintenance/Engineering Mode
    Soft Reset
    Purge Time
    Vac System Reset
    Gantry PID Tune Loop
    Password Change

## Slide 3
Contents
6. Manual Operations
  Gantry Manual Controls
    Jogging
  Conveyors
  Filter Plate Manual Controls
    Plate Axis On/Off
  Press Manual Controls
    Maintenance Position
7. Homing Sequence
  Trash Collection
8. Run Sequence
  Start/Stop Process
9. Errors and Troubleshooting
  Error Screen
  Error Description
  Troubleshooting
10. Other Features

## Slide 4
First Time Startup
Operation Description
After initial installation of the filter press. All machine move positions will need to be setup and fine tuned within the HMI.
Not doing so can result in machine damage and inaccurate move positions during a production run. All units are in MM(millimeters) or MM/s millimeters per second.
The following positions need to be setup in sequential order to achieve best results:
  Gantry Arm
    In Conveyor Pickup Position
    Out Conveyor Pickup Position
    Gripper 1 Shuttle Position
    Gripper 2 Shuttle Position
    Gripper 1 Used Product
    Gripper 2 Used Product
    Gantry Speed in mm/s
  Press and Press Lift
    Lift up position
    Lift down position
    Press maintenance position
    Press ready position
    Press “Pressed” position
    Press and Lift Speeds in mm/s
  Filter Plate
    Filter plate 1st hole position
    Filter plate lock pin position
    Filter plate feeding speed in mm/s

## Slide 5
First Time Startup
  Conveyors
    Input and output conveyor speeds mm/s

## Slide 6
Home Screen Layout
Machine errors screen
Manual mode button
Auto mode button
Engineering and maintenance
mode status indicators
Manual controls screen
Settings screen
Machine status indicator
Cycle stop/start process button
Home status indicator
Quantity of units produced
Home all button
The home screen is presented on machine startup. Below is a description of each item on the home screen. Refer to the Run Sequence for auto operations.

## Slide 7
Engineering and
maintenance mode buttons
Settings Screen Layout
On the settings screen, each component can be selected individually for adjustment.

## Slide 8
Maintenance / Engineering Mode
  Conveyors
    Input and output conveyor speeds mm/s

## Slide 11
Engineering Mode